## Slide 1: Development of Image Analysis Algorithms for Crack Detection Using a Smartphone Mounted in a Car (SnapCrack)
By: Akira DeMoss, Maggie Dalton, Modeste Kenne, Nik Thota
Advisor: Halil Ceylan
Client: Bo Yang
Team Name: sdmay20-18
Website: http://sdmay20-18.sd.ece.iastate.edu/
Notes: Modeste

## Slide 2: Project Need/Goal
Problem: The detection and classification of cracks and potholes found on roads currently require a manual measurement of the affected areas. Researchers have to exit their vehicles and enter the roadway, which is often dangerous and time consuming.
Project Goal: Remove the need for researchers to leave their vehicles to gather data.
Methodology: Use a smartphone mounted in a vehicle to gather and classify data using machine learning algorithms.
Notes: Modeste

## Slide 3: Market/Literature Survey
Mobilenet SSD has been used to detect various road anomalies including alligator cracking, crosswalks
YOLO has been used on a desktop to detect various road anomalies.
Publically available datasets
Notes: Akira

## Slide 4: Our Solution
Detect cracks in real-time using mobile-device powered object detection
Send images to a server and store in database
Visualize crack locations and modify labels through a web application
Notes: Akira

## Slide 5: Functional Requirements
Android Application
  Detect potholes, longitudinal and transverse cracks
  Save images of detected cracks to the server, including their location
API
  Provide detailed API error responses
User Interface
  The app should not require any further interaction from the user once the road scan begins
  The app should display bounding boxes around detected cracks/potholes to provide visual feedback of detections
Notes: Modeste

## Slide 6: Non-functional Requirements
Android Application
  Detect cracks/potholes on various types of roads
  Detect cracks/potholes at multiple driving speeds
  Classify cracks/potholes per the Long-Term Pavement Performance Program (LTPP) distress manual
API:
  The API should have documentation for each endpoint
User Interface
  If the classification server is not available, the user interface should display a message indicating a loss of communication to the user
  The user should be capable of viewing past detections along with their data
Notes: Modeste

## Slide 7: Risk Identification & Mitigation
Notes: Akira

## Slide 8: Use Cases
Notes: Maggie

## Slide 9: Functional Decomposition
Notes: Maggie, referenced https://www.tutorialspoint.com/software_testing_dictionary/functional_decomposition.htm and sddec19-14’s presentation

## Slide 10: Resources/Cost Estimate
Android Device → API 27+ ~ Google Pixel 4 XL $600
3rd Party Phone Mount ~ $20 - $25
Computer with Node.js and MySQL installed
  Images stored on filesystem
Web Browser

## Slide 11: Project Milestones & Schedule
Snapcrack - Sdmay20-18

## Slide 12
Snapcrack - Sdmay20-18

## Slide 13: Detailed Design / Modules Design
Notes: Nik

## Slide 14: Build - Platforms & Technologies
Android
  TensorFlow Lite
  Volley
  Java/Kotlin
Web Portal
  React
  JavaScript/HTML/CSS
Back-End
  Ubuntu VM
  MySQL
  Node.js
Algorithm
  TensorFlow
  OpenCV
  CUDA
Notes: Maggie

## Slide 15: Implementation Detail -> Algorithm
Standard convolution both filters and combines inputs into a new set outputs in one step
Depthwise Separable Convolution (DSC) splits this into two layers
  Filtering layer
  Combining layer
SSD Mobilenet leverages the DSC module for feature extraction and the base architecture of the Single Shot Detector to achieve fast real-time detection on mobile devices.
Convolutional Neural Network Architecture: SSD Mobilenet
Notes: Akira

## Slide 16: Implementation Detail -> Android Application
TensorFlow Lite
  Allows on-device inferencing
Android CameraX Library
  Greater support for ML
Volley Library
  Easier & Faster HTTP Requests
Notes: Maggie

## Slide 17: Implementation Detail -> Backend/Web Portal
Node.js Server
  Non-blocking
  Fast
MySQL Database
  Easy to use and install
React
  Easier, more professional UI

## Slide 18: User Interface Design
Sleek and Simple Design
Notes: Nik

## Slide 19: How We Tested
Datasets
Training data: 1405 images, 3055 labels
Testing data: 350 images, 756 labels
Mean Average Precision (mAP) Performance Benchmark
Intersection over Union (IoU) = Area of intersection / Area of union
True positive (TP): IoU > 0.5
False positive (FP) IoU <= 0.5
Precision = TP / (TP + FP)
Mean Average Precision (mAP) =
Notes: Akira

## Slide 20: Testing
Notes: Akira

## Slide 22: Prototype vs. Final Product
Prototype:
Proof of concept for object detection
Was able to make some detections when tested on videos from Iowa
Pre-existing dataset contained extraneous and mislabeled data
Final Product:
Detect cracks in real-time using mobile-device powered object detection
Send images to a server and store in database
Visualize crack locations and modify labels through a web application
Notes: Akira

## Slide 23: Design Tradeoffs
Speed vs. Accuracy Tradeoff
  Pros
    Faster detections
    Real-time detection
    Improved scalability
    Improved usability
    Positive developer experience
  Cons
    mAP could be higher
Notes: Akira

## Slide 24: Conclusions & Lessons Learned
Our project may prove to be useful to civil engineers wishing to survey road conditions
Trimmed features to stick to schedule and keep realistic expectations
  Removed severity classification
  Gave us more time to focus on more important functions
Our project came together well, however there is potential for improvement
Notes: Nik

## Slide 25: Engineering Standards & Design Practices
Standardized Tooling and Technologies
  Agreed on tools and technologies
Standardized Coding Style
  Defined conventions for coding
Process Standards
  Agreed on development steps
Notes: Modeste

## Slide 26: Responsibilities
Akira Demoss: Deep Learning Developer
Maggie Dalton: Android Developer
Modeste Kenne: Server Developer
Nik Thota: Web Developer
All: Image gatherer/labeler
Notes: Modeste

## Slide 27: Future Work
Potential updates with a more accurate model
Severity classification
More crack types
  Alligator
  Fatigue
  Fillings
Specific crack identified in
web portal
Test with civil engineers and consider their feedback
Notes: Nik

## Slide 28
Questions?